## Slide 1: Smart Door Lock HSLU - IOT
Boas Meier, Niklas Tanner, Lukas Mettler, Tobias Heller
Rotkreuz, 05.02.2022

## Slide 2: Table of Contents USECASE 01 SOLUTION 02 NEXT STEPS 03 DEMO 04
Why is a smart door lock needed?
How did we solve it and what were the biggest challenges?
What are our next steps?
How does our product work?

## Slide 3: USECASE 01

## Slide 4: Features
Door lock
Lock, Unlock
Remote access
Door bell
Ringing
Remote Push
Security
Alarms, Intrusion
Suspicious Activities
Remote Push

## Slide 5: User Interfaces
Web Application
State of door
Previous actions
Remote actions
Mobile App
Open with NFC
Receive notifications
Unlock remotely
Human Machine
Interface
LED Red / Green
Button
Notes: LED
NFC Chip Ok: Kurz Grün oder Rot
Wenn Tür geöffnet: Leuchtet Grün

## Slide 6: SOLUTION 02

## Slide 7: System overview

## Slide 8: 11
Number of main software components

## Slide 10: Functional Software Architecture
Notes: But how do they interact?

## Slide 11: But what if it doesn’t?

## Slide 12: Elastic Stack
Elasticsearch, Kibana and Integrations
Notes: What is the Elastic Stack?
  Definition of Components
What it is for…
How it works in our Environment

## Slide 13: What is the Elastic Stack?

## Slide 14: What we use it for
Log collection at Edge Device (Edge Agent, Door Controller, Edge Device itself (filesystem logs))
Log collection (metric data) at Cloud / Backend (all containers)
Why?
Monitoring
Transparency
Troubleshooting

## Slide 15: Technical challenges
And how we solved them

## Slide 16: Interrupts and Reentrancy
Super-Loop vs. Event-Loop vs. RTOS
Mqtt messages and GPIO signals trigger interrupts
Actual work is done in main-loop and not inside ISR -> Set an interrupt flag (event)
Notes: No RTOS because we don’t need to do many things in parallel
No Super-Loop because we don’t want to miss any signals
Event-Loop program is controlled over Interrupts and Events
To keep interrupt latency small we only set a flag inside the ISR and process the interrupt in the main-loop
Problem: Interrupt Flag is accessed from main-loop and from ISR -> possibility for Race Conditions

## Slide 17: Interrupts and Reentrancy
static volatile byte interruptFlag = 0;
Use volatile to tell the compiler to not optimize any line of code containing the interruptFlag.
Use byte for atomic access, since Arduino Uno Wifi Rev2 usese an 8-bit mcu (ATmega4809).
Source: https://ww1.microchip.com/downloads/en/DeviceDoc/ATmega4808-09-DataSheet-DS40002173C.pdf (p.39)
ATmega4808 Memory Map
8 bit
Notes: Solution: Access to Interrupt Flag needs to be reentrant -> Use of Critical Sections or use 8-bit type (e.g. byte) because an 8-bit microprocessor (ATmega4809) is used. Acceess to 8-bit types are atomic (done in one instruction)
Problem: Compiler somehow optimizes away interrupt flag, since its only incremented from inside the ISR.
Solution: Use volatile keyword to tell the compiler to not optimize any line of code which contains the interrupt flag

## Slide 18: Interrupts and Reentrancy
#include <util/atomic.h>
void PahoMqttClient::handleMqttMessage() {
int n = QUEUE_SIZE;
ATOMIC_BLOCK(ATOMIC_RESTORESTATE) {
if(mqttMessagePointerQueue[0] != -1) {
MqttMessageHandler::handleMessage(mqttMessagePointerQueue[0]->getTopic(),
mqttMessagePointerQueue[0]->getMessage());
for(int i=0; i<n-2; i++) {
mqttMessagePointerQueue[i] = mqttMessagePointerQueue[i+1];
}
mqttMessagePointerQueue[n-1] = (MqttMessage*) -1;
}
}
}
Disbale Interrupts
Enable Interrupts again
Critical Section

## Slide 19: NEXT STEPS 03

## Slide 20: Next steps
Features
  Improved App (Android & iOS)
  Camera Streaming
Security (IAM, IDS/IPS, TLS, …)
Zero-Touch Deployment

## Slide 21: DEMO 04
Notes: Währenddessen WEB GUI und

## Slide 22: Local unlock with card

## Slide 23: Local unlock with phone

## Slide 24: Ring and remote unlock with phone

## Slide 25: Suspicious activity with rejected card
Notes: Bewegungssensor erst jetzt anhängen
Becher abdecken

## Slide 26: Intrusion with alarm

## Slide 27: Remote unlock with web interface
Notes: - Web Interface zeigen

## Slide 28: Filtering with Kibana

## Slide 29: Questions?